## Slide 1: Presented by Jaghdish Battu
MASS SPECTROMETRY
Dept.of Chemistry
Avanthi Degree & P.G College

## Slide 2: Mass Spectrometry
Introduction
  General overview
    Mass Spectrometry is the generation, separation and characterization of gas phase ions according to their relative mass as a function of charge
    Previously, the requirement was that the sample be able to be vaporized (similar limitation to GC), but modern ionization techniques allow the study of such non-volatile molecules as proteins and nucleotides
    The technique is a powerful qualitative and quantitative tool, routine analyses are performed down to the femtogram (10-15 g) level and as low as the zeptomole (10-21 mol) level for proteins
    Of all the organic spectroscopic techniques, it is used by more divergent fields – metallurgy, molecular biology, semiconductors, geology, archaeology than any other

## Slide 3: Mass Spectrometry
I. The Mass Spectrometer
  General Schematic
    A mass spectrometer needs to perform three functions:
      Creation of ions – the sample molecules are subjected to a high energy beam of electrons, converting some of them to ions
      Separation of ions – as they are accelerated in an electric field, the ions are separated according to mass-to-charge ratio (m/z)
      Detection of ions – as each separated population of ions is generated, the spectrometer needs to qualify and quantify them
    The differences in mass spectrometer types are in the different means to carry out these three functions
    Common to all is the need for very high vacuum (~ 10-6 torr), while still allowing the introduction of the sample

## Slide 4: Mass Spectrometry
The Mass Spectrometer
  Single Focusing Mass Spectrometer
    A small quantity of sample is injected and vaporized under high vacuum
    The sample is then bombarded with electrons having 25-80 eV of energy
    A valence electron is “punched” off of the molecule, and an ion is formed

## Slide 5: Mass Spectrometry
The Mass Spectrometer
  The Single Focusing Mass Spectrometer
    Ions (+) are accelerated using a (-) anode towards the focusing magnet
    At a given potential (1 – 10 kV) each ion will have a kinetic energy:
        ½ mv2 = eV
      As the ions enter a magnetic field, their path is curved; the radius of the curvature is given by:
      r = mv
      eH
      If the two equations are combined to factor out velocity:
      m/e = H2r2
      2V
m = mass of ion
v = velocity
V = potential difference
e = charge on ion
H = strength of magnetic field
r = radius of ion path

## Slide 6: Mass Spectrometry
The Mass Spectrometer
  Single Focusing Mass Spectrometer
    At a given potential, only one mass would have the correct radius path to pass through the magnet towards the detector
    “Incorrect” mass particles would strike the magnet

## Slide 7: Mass Spectrometry
The Mass Spectrometer
  Single Focusing Mass Spectrometer
    By varying the applied potential difference that accelerates each ion, different masses can be discerned by the focusing magnet
    The detector is basically a counter, that produces a current proportional to the number of ions that strike it
    This data is sent to a computer interface for graphical analysis of the mass spectrum

## Slide 8: Mass Spectrometry
II. The Mass Spectrum
  A. Determination of Molecular Mass
    When a M+ peak is observed it gives the molecular mass – assuming that every atom is in its most abundant isotopic form
    Remember that carbon is a mixture of 98.9% 12C (mass 12), 1.1% 13C (mass 13) and <0.1% 14C (mass 14)
    We look at a periodic table and see the atomic weight of carbon as 12.011 – an average molecular weight
    The mass spectrometer, by its very nature would see a peak at mass 12 for atomic carbon and a M + 1 peak at 13 that would be 1.1% as high

## Slide 9: Mass Spectrometry
The Mass Spectrum
  Determination of Molecular Mass
    Some molecules are highly fragile and M+ peaks are not observed – one method used to confirm the presence of a proper M+ peak is to lower the ionizing voltage – lower energy ions do not fragment as readily
    Three facts must apply for a molecular ion peak:
      The peak must correspond to the highest mass ion on the spectrum excluding the isotopic peaks
      The ion must have an odd number of electrons – usually a radical cation
      The ion must be able to form the other fragments on the spectrum by loss of logical neutral fragments

## Slide 10: Mass Spectrometry
II. The Mass Spectrum
  Determination of Molecular Mass
    The Nitrogen Rule is another means of confirming the observance of a molecular ion peak
    If a molecule contains an even number of nitrogen atoms (only “common” organic atom with an odd valence) or no nitrogen atoms the molecular ion will have an even mass value
    If a molecule contains an odd number of nitrogen atoms, the molecular ion will have an odd mass value
    If the molecule contains chlorine or bromine, each with two common isotopes, the determination of M+ can be made much easier, or much more complex as we will see

## Slide 11: Mass Spectrometry
III. The Mass Spectrum and Structural Analysis
  Inferences from Isotopic Ratios
    For molecules that contain Cl or Br, the isotopic peaks are diagnostic
      In both cases the M+2 isotope is prevalent:
        35Cl is 75.77% and 37Cl is 24.23% of naturally occurring chlorine atoms
        79Br is 50.52% and 81Br is 49.48% of naturally occurring bromine atoms
      If a molecule contains a single chlorine atom, the molecular ion would appear:
m/e
relative abundance
M+
M+2
The M+2 peak would be 24% the size of the M+
if one Cl is present

## Slide 12: Mass Spectrometry
The Mass Spectrum and Structural Analysis
  Inferences from Isotopic Ratios
    For molecules that contain Cl or Br, the isotopic peaks are diagnostic
      b) If a molecule contains a single bromine atom, the molecular ion would appear:
      c) The effects of multiple Cl and Br atoms is additive – your text has a complete table of the combinations possible with 1-3 of either atom
    d) Sulfur will give a M+2 peak of 4% relative intensity and silicon 3%
m/e
relative abundance
M+
M+2
The M+2 peak would be about the size of the M+
if one Br is present

## Slide 13: Mass Spectrometry
The Mass Spectrum
  Presentation of data
    The mass spectrum is presented in terms of ion abundance vs. m/e ratio (mass)
    The most abundant ion formed in ionization gives rise to the tallest peak on the mass spectrum – this is the base peak
base peak, m/e 43

## Slide 14: Mass Spectrometry
The Mass Spectrum
  Presentation of data
    All other peak intensities are relative to the base peak as a percentage
    If a molecule loses only one electron in the ionization process, a molecular ion is observed that gives its molecular weight – this is designated as M+ on the spectrum
M+, m/e 114

## Slide 15: Mass Spectrometry
The Mass Spectrum
  Presentation of data
    In most cases, when a molecule loses a valence electron, bonds are broken, or the ion formed quickly fragment to lower energy ions
    The masses of charged ions are recorded as fragment ions by the spectrometer – neutral fragments are not recorded !
fragment ions

## Slide 16
M+
M+2
Base peak ,m/e =28
Molecular ion, m/z =64

## Slide 17
Mass spectrum of Ethyl bromide

## Slide 18
Molecular ion at m/z=120
Base peak at m/z=105

## Slide 19
THANK YOU